## Slide 2: CE 437 – Timber Design

## Slide 3: CE 437 – Timber Design
Project: Playground
Dave Maruskin (el capitan)
Jason Huck (resident architect)
Jeff Leake (interior design)
Bryan Dhume (special joint designer)
Jason Manson (chief carpenter)
Zach Bazell (CAD technician)

## Slide 4: Timber Design Project
  Objective: To design and analyze a timber playset using Load and Resistance Factor Design

## Slide 8: CE 437 – Timber Design
Project: Playground
Dave Maruskin (el capitan)
Jason Huck (resident architect)
Jeff Leake (interior design)
Bryan Dhume (special joint designer)
Jason Manson (chief carpenter)
Zach Bazell (CAD technician)

## Slide 9: Specifications
- Access to shelter by ladder and railing for safety
- All members used are pressure treated Southern yellow pine
- Two structures connected by a bridge: housed and platform portions
- Each portion is 8 x 8 ft. and 8 ft. high
4 ft. walkway around shelter
- Roof covers an area of 16 x 16 ft. with a pitch of 12 on 12

## Slide 10: Loads Applied (unfactored)
Dead Load (self-weight): 50 lb./ft.3
Live Load (roof): 12 lb./ft.2
Live Load (deck): 50 lb./ft.2
Snow Load (roof): 21.2 lb./ft.2
Snow Load (deck): 30 lb./ft.2
Wind Load (leeward side): 3.9 lb./ft.2
Wind Load (windward side): 6.25 lb./ft.2
Wind Load (roof lateral): 5.47 lb./ft.2
Shingles: 3 lb./ft.2

## Slide 11
Major Vertical Members
- 4 x 4 posts at 12 feet long posts supporting platform
- 6 x 6 at 16 feet long for housed portion
- 4 x 4 king posts supporting roof truss

## Slide 12
Elevation View

## Slide 13
Elevation View – Bent 3

## Slide 14
Elevation View – Bent 4

## Slide 15
Major Horizontal Members
- 4 x 8 ridge beam at 16 feet long
- 4 x 6 fascia beams at 16 feet long
- 4 x 4 for truss rafters, chords
- 2 x 8 girts and joists on platform
- 2 x 8 joists in housed portion

## Slide 16
Plan View – Bottom of Truss

## Slide 17
Plan View – Deck

## Slide 18
Other Materials
- 1” plywood sheathing
- 2 x 6 tongue-in-groove decking
- 2 x 4 kneebraces
- 2 x 6 bridge girts
- 4 x 4 verticals and 2 x 4 horizontals for railing
- 2 x 6 patio joists

## Slide 19
Connections
- Posts secured to concrete with anchors
- Girt connections utilize housed mortise and tenon
- Extensive use of joint hangars
- Truss constructed with fabricated gusset plate

## Slide 20
Detail – Post Anchor

## Slide 21
Detail – Mortise & Tenon Joint/Joist Hangars

## Slide 22
Detail – Truss Gusset Plate

## Slide 23
SAP 2000 – Finite Element Analysis
- Structure treated as frame (connections transfer moment)
Support connections assumed pinned
Load factors applied:
    Dead Load - 1.2
    Live Load - 1.6
    Snow Load - 0.5
    Wind Load - 0.7

## Slide 24
Axial Forces
Maximum Factored Loads:
Rafters: 1.5 kips (tension)
Bottom Chords of Truss: 1.4 kips (compression)
Kneebraces: 1.0 kips (compression)
L.R.F.D. Design Values:
Rafters (4 x 4): 17.5 kips (tension)
Bottom Chords of Truss (4 x 4) , 6’ unbraced: 10.2 kips (compression)
Kneebraces (2 x 4): 7.1 kips (compression)
4 x 4
4 x 4
4 x 4
4 x 4
2 x 4

## Slide 25
Moment 2-2
Maximum Factored Loads:
Columns: 4.0 in.-kips
L.R.F.D. Design Values:
Columns (6 x 6) : 40.7 in.-kips
6 x 6
6 x 6
6 x 6

## Slide 26
Axial Forces
Maximum Factored Loads:
King Post: 5.0 kips (compression)
Columns: 5.5 kips (compression)
L.R.F.D. Design Values:
King Post (4 x 4) , 8’ unbraced: 10.2 kips
Columns (6 x 6) , 8’ unbraced: 23.4 kips (compression)
6 x 6
6 x 6
6 x 6
6 x 6
4 x 4
4 x 4

## Slide 27
Moment 3-3
Maximum Factored Loads:
Ridge Beam: 53.0 in.-kips
L.R.F.D. Design Values:
Ridge Beam (4 x 10) : 99.7 in.-kips
4 x 8

## Slide 28
Shear 2-2
Maximum Factored Load:
Ridge Beam: 2.8 kips
L.R.F.D. Design Values:
Ridge Beam (4 x10) : 3.37 kips
4 x 8

## Slide 29
Axial Forces
Maximum Factored Loads:
Columns: 3.9 kips
Posts: 1.8 kips
L.R.F.D. Design Values:
Columns (6 x 6) , 6’ unbraced: 25.4 kips
Posts (4 x 4) , 8’ unbraced length: 10.2 kips
6 x 6
6 x 6
6 x 6
4 x 4
4 x 4

## Slide 30
Moment 2-2
Maximum Factored Loads:
Fascia Beam: 9.8 in.-kips
Fasica Beam , Moment 3-3: 23.0 in.-kips
L.R.F.D. Design Values:
Fascia Beam (4 x 6) : 24.3 in.-kips
Fascia Beam (4 x 6) , Moment 3-3 : 38.2 in.-kips
4 x 6
4 x 6

## Slide 31
Deformation due to Dead Load
Deformation due to Live Load
Deformation due to Snow Load
Deformation due to Wind Load

## Slide 32: Quantities of Material Used

## Slide 33: Cost of Materials

## Slide 34: Connector Cost Breakdown

## Slide 35
The End